## Slide 1
Deamidation of Asparaginec
In general, when Asparagine residue is deamidated, the amine group (-NH2) of Asparagine residue is replaced by a hydeoxyl group (-OH). Therefore, the deamidation process results in a +0.9840 mass shift.
In our samples, there are two ways to have a deamidation modification on Asparagine residue. One is due to the PNGase F digestion, another is a natural process which could occur in the sample preparation. Both of them will result in a +0.9840 mass shift on N. However, PNGase F will only modify the N when it is linked with a N-glycan. In other words, PNGase F will only modify the N in the NXS/T motif.

## Slide 2
MASCOT Search of Deamidation of Asparagine
In MASCOT search, we can not distinguish the two type of deamidation. We only search for +0.9840 mass shift on N residues. Therefore, it will create a problem with the glycopeptide mass calculation.
In general, the glycopeptide mass = peptide mass + glycan mass – H2O (18.0105).
For example, the mono isotopic mass of glycopeptide NLTK+2500 =
474.2802 (peptide mass) + 2*203.0794 +5*162.0528 +18.0105(glycan mass) – 18.0105 = 1690.7030
However, in the PNGase F sample, since all the N-linked glycosylation site was deamidated, all the occupied NXS/T motifs are changed to DXS/T. Therefore, the MASCOT result of calculated peptide mass is off by 0.9840.
For example, the mass of SLVTQYLNATGNR is 1435.7419. When you calculate the glycopeptide mass of this peptide backbone, you should use 1435.7419 as your peptide backbone mass. However, in the MASCOT search file, the mass is 1436.7259 (1435.7419+0.9840). If you use 1436.7259 as the peptide mass, the result will be off by 0.9840.
pep_calc_mr | pep_res_before | pep_seq | pep_res_after | pep_var_mod | pep_var_mod_pos
1436.726 | K | SLVTQYLNATGNR | W | Deamidated(N) (N) | 0.0000000200000.0

## Slide 3
If the deamidation is not caused by PNGase F, then you will take the +0.9840 in you calculation of glycopeptides.
For example, peptide TVTISDHGTVTYN(1)GSICGDDQN(2)GPK has 2 Ns. N(1) is a glycosylation site, N(2) is not. In the MASCOT result, two forms of deamidation are detected. One is only N(1) deamidation, the other is both site deamidation.
pep_calc_mr | pep_res_before | pep_seq | pep_res_after | pep_var_mod | pep_var_mod_pos
2636.166 | K | TVTISDHGTVTYNGSICGDDQNGPK | I | Deamidated(N) (N) | 0.0000000000002000000000000.0
2637.15 | K | TVTISDHGTVTYNGSICGDDQNGPK | I | 2 Deamidated(N) (N) | 0.0000000000002000000002000.0
In this case, N(1) deamidation is due to PNGase F digestion, while N(2) deamidation is a random natural process.
Therefore, when you calculate the glycopeptide mass, for the N(1) deamidation form, the peptide backbone mass is 2635.1820 (2636.166-0.9840).
For the N(1)&N(2) deamidation form, you do NOT substract 2*0.9840, because the N(2) deamidation is not caused by PNGase F. The mass of the second peptide backbone is 2636.166 (2637.15-0.9840).

## Slide 4
Extra Rule
Since the PNGase F will digest the N-glycan from the N residue and change it to D through deamidation (+0.9840). We consider this reaction is 100% complete. Therefore, for any peptide has the motif NXS/T, if the N in the motif is not deamidation in the PNGase F sample, we will consider this glycosylation site is not occupied. Therefore, this peptide could be eliminate from the candidate list.
In addition, since the N deamidation could occur during sample preparation, we would like N deamidation to be a variable modification.

## Slide 5
Summary
For any peptide from the MASCOT result,
AAAAAN(1)XS/TAAAAAN(2)AMAACAAK,
For N residue,
i. If N(1) is not detected to be deamidated, then exclude this peptide from candidate list.
ii. If N(1) is deamidated, no matter the N(2) deamidated or not, then take the mass from “pep_calc_mr” column and substract 0.9840 as the peptide back bone mass.
iii. If there are multiple N(1)s (glycosylation sites) detected, x of the N(1)s are deamidated, then take the mass from “pep_calc_mr” column and substract x *0.9840 as the peptide back bone mass.
iv. For N(2) deamidation, please treat it as a variable modification. (If only deamidated N(2) is detected, then create an native one (-0.9840). If only native N(2) is detected, then create a deamidated one(+0.9840))
For M residue,
i. If M is detected as native M, then create a variable modification of O (+15.9949).
ii. If M is detected as oxidation form, then create a variable modification of native form (-15.9949).
iii. If M is detected as Carbamidomethylated M, then create the native form (-57.0215) and the oxidated form
(-57.0215+15.9949).
For C residue,
Always keep Carbamidomethylated C as a fixed modification.